## Slide 1
SMART APS V11
Constraint Architecture & Solution Design
Advanced Production Scheduling System
11 Constraints
Multi-Machine
Color-Aware
Terminal-Aware
Real-Time State
Planning Date: April 2026 | Version: V11-FIXED | Deterministic Output

## Slide 2
SYSTEM OVERVIEW — Constraint Landscape
C1
Minimum Run
Hours
C2
Daily Indent
Skip Rule
C3
Inventory
Ceiling (OPD)
C4
Terminal
Inventory
C5
Fixed Machine
Constraint
C6
Color Purge
Changeover
C7
Max Daily
Changeovers
C8
Tool Availability
Limit
C9
Runner Priority
Lock
C10
22H Utilization
Target
C11
Tool-Changer
Queue
11 Active Constraints govern every scheduling decision in Smart APS V11

## Slide 3
MASTER SCHEDULING PIPELINE
Load Inputs
(Inventory, Indent,
Matrix, State)
Classify
Scenario
(0-3)
Fixed Machine
Pass
(Phase A/B)
Priority
Scoring
& Sorting
Primary
Assignment
Pass
Runner
Priority
Enforcement
22H
Utilization
Enforcer
Strategic
Buffer
Filler
Resequence
(CO minimize)
CO Stagger
(Tool Changer
Queue)
Validate
& Flag
Violations
Forward
Look
(7-day Alert)
Save
Machine
State
Excel
Output
(19 sheets)

## Slide 4
C1 & C2 — Skip Rules: Minimum Run Hours & Daily Indent Thresholds
C1 — Minimum Run Hours (MIN_RUN_HOURS = 4h)
Part candidate
for scheduling
Free hrs − CO hrs
≥ MIN_RUN_HOURS (4h)?
YES
NO
Schedule & run
part on machine
Skip
this
machine
Why 4 hours? Running a mold for less than 4h is economically inefficient — setup overhead consumes too much of the available production window. CO time is subtracted from available hours before this check applies.
C2 — Daily Indent & Monthly Indent Skip Rules
Daily indent
≤ 150 pcs?
SKIP — too low demand
NO
Monthly indent
÷ rate ≤ 4 hrs?
SKIP — full monthly = micro run
NO
Inventory ≥
5-day target?
SKIP — at ceiling, rest
All checks
PASS

## Slide 5
C3 — Inventory OPD Ceiling (Scenario-Based Production Cap)
S0
ALL parts critical
(inventory < 1 day)
OPD Cap: 3.0 days
S1
Some parts critical,
others have buffer
OPD Cap: 3.0 days
S2
Parts below
3-day safety floor
OPD Cap: 4.0 days
S3
All parts healthy
(≥ 3-day floor)
OPD Cap: 5.0 days
HOW THE CAP IS APPLIED
Compute
cap_qty
= OPD × daily
Headroom
= cap_qty
− inventory
Run hours
= min(free,
headroom/rate)
Machine
hours
updated
Inventory
simulation
updated
Key principle: The OPD (Outstanding Production Days) cap prevents over-stocking by capping production at N×daily_indent per part. Scenario determines N (3–5 days). Machines are filled up to the OPD ceiling, never beyond — preserving machine time for other critical parts. Safety_Days=3, Target=5 days.

## Slide 6
C4 — Terminal Inventory Constraint (Hard Block)
What is a Terminal?
Terminals are downstream raw-material components required to produce a part. Each part may require one or more specific terminals. If a terminal's inventory falls below the threshold, the part is HARD-BLOCKED from scheduling.
Threshold by Part Category
Category
Multiplier
Min Terminal Stock
Runner
1.0×
= 1.0 × daily indent
Repeater
0.5×
= 0.5 × daily indent
Stranger
0.25×
= 0.25 × daily indent
TERMINAL CHECK FLOWCHART
Part has
required terminals?
Look up terminal
inventory
inv ≥ threshold
for all terminals?
PASS — include
in scheduler
HARD BLOCK
(not planned)
FAIL
PASS

## Slide 7
C5 — Fixed Machine Constraint (Phase A / Phase B Logic)
PHASE A — Buffer Building (CRITICAL)
Triggered when ANY fixed part on machine has inventory < 3-day safety floor
Machine runs the single MOST URGENT fixed part for the entire shift
Run hours = full AVAILABLE_HOURS (up to 23h if indent is very high)
No other parts compete — machine is exclusively locked
Part with lowest days_coverage is chosen (tie-broken by higher hours needed)
PHASE B — OPD Build (NORMAL)
Triggered when ALL fixed parts on machine are above safety floor
EACH fixed part runs for its specific daily indent hours (min 4h)
OPD ceiling applies — headroom = cap_qty − current_inventory
Multiple fixed parts can run on the same machine in Phase B
Remaining machine hours released for general scheduler pool
Phase determined at run time by checking live inventory of all parts assigned to that machine

## Slide 8
C6 & C7 — Color Purge Changeover & Max Daily Changeovers
C6 — Color Purge Changeover
RED
RED
Base CO only (no purge)
RED
BLUE
Base CO + 10min purge
UNKNOWN
ANY
Base CO only (unknown = no purge)
COLOR_PURGE_HRS = 10 min (0.167h)
Purge is added ONLY when both from/to colors are known and differ. Machine state tracks last run part for each machine.
C7 — Max Daily Changeovers (MAX_DAILY_CO = 25)
The Tool Changer is a SERIAL RESOURCE — only one CO can physically occur at a time. Limiting to 25/day prevents: • Excessive tool-changer queue buildup • CO collisions causing idle machine time • Operator overload Enforcement: Before adding any new CO-requiring assignment, the scheduler checks _current_co_count(plan) ≥ 25. If at cap, only no-CO additions are permitted.
TOOL CHANGER QUEUE (serial)
CO#1
+40min
CO#2
+40min
CO#3
+40min
...
CO#25
max

## Slide 9
C8 & C9 — Tool Availability Limit & Runner Priority Lock
C8 — Tool (Mould) Availability Limit
Each part has a fixed number of tools (moulds) available. A part can run on at most TOOLS_AVAILABLE machines simultaneously:
Runner (Critical)
Up to min(2, tools) machines
Repeater / Stranger
Max 1 machine always
Any (ZERO inventory)
Force up to tools limit
Tool expansion tracks used_machines set per part. Once tool cap is reached, no more machines are added for that part that day.
C9 — Runner Priority Lock & Displacement
Runner part
unplanned today
Inventory <
2× daily indent?
Find machine
with free capacity
PLAN Runner
on free machine
No free capacity?
Displace low-priority part
Runner placed
via displacement
FREE
NO
FREE
Displacement carves hours from Stranger/Repeater parts with higher coverage than the Runner. Victims yield time proportionally, never below MIN_RUN_HOURS.

## Slide 10
C10 — 22H Utilization Enforcer (5-Stage Pipeline)
S0
Extend to
90% Floor
Extend existing parts on this machine until utilization ≥ 90% of 22h.
S2
Add New
Parts
Add unplanned compatible parts with CO awareness. Prefer same color, no CO.
S1
Progressive
Ceiling Ext.
Extend existing parts through OPD → 7-day → 15-day ceilings sequentially.
S3
Runner
Spare Tool
Assign spare tool for a Runner that still has indent unmet and capacity.
S4
Any Compatible
Part
Fill with any compatible part up to absolute max (15-day cap).
S5
Final
Tail Fill
Last-pass extension to fill remaining micro-idle to 15-day ceiling.
MACHINE UTILIZATION BAR — BEFORE vs AFTER ENFORCER
Before:
Planned ~60%
IDLE
After:
Fully utilized ≥ 95% (S0→S5 applied)
min idle

## Slide 11
C11 — Tool-Changer Serial Queue & CO Stagger
Problem: The tool-changer robot is a SINGLE serial resource. Multiple machines cannot perform changeovers simultaneously. Without staggering, parallel COs on different machines would collide, causing machine idle time equal to waiting for the tool changer.
TOOL CHANGER TIMELINE (Serialized CO Queue)
Machine A
Machine B
Machine C
Part X running
CO
40min
Part Y running
Part A running
WAIT
+ext
CO
40min
Part B running
Part P running
WAIT (extended)
CO
40min
Part Q running
Production run
CO (tool changer)
Wait/extension
While waiting, the machine extends its BEFORE-CO part production — zero idle time. CO stagger resolves conflicts so tool changer is never double-booked.

## Slide 12
PRIORITY SCORING ENGINE — How Parts Are Ranked
Final Score = 0.55 × Urgency Score + 0.25 × Category Score + 0.20 × Indent Score
URGENCY SCORE (55%)
0.60 × gap_pct + 0.40 × velocity_pct
gap_pct: how far inventory is from the 5-day target ceiling
velocity_pct: daily indent / max inventory ratio across all parts
Parts with zero or very low inventory score near 100%
CATEGORY SCORE (25%)
Runner=100 | Repeater=60 | Stranger=20
Runner: highest priority — supply chain must never run dry
Repeater: medium priority — planned but flexible
Stranger: lowest — scheduled only when capacity is available
INDENT SCORE (20%)
(daily_indent / max_daily) × 100
Parts with high daily indent get proportionally higher scores
Rewards high-volume, high-commitment production
Normalized to 0–100 scale across all active parts
Parts are sorted by Final_Score (descending) before assignment — deterministic tie-breaking by part name ensures reproducible plans

## Slide 13
MACHINE SELECTION & RANKING — How a Machine is Chosen
Ranking Cost = count_score + CO_penalty + utilization_penalty + same_part_bonus + color_bonus → Lowest cost wins
Part Count
Score
part_count / max_part_count
Prefer machines that can run fewer part types (more specialized)
CO Penalty
(co_hrs / 22) × 0.3
Higher changeover time = higher penalty. Same-color avoids purge adder.
Utilization
Penalty
(used_hrs / 22) × 0.2
Prefer less-used machines to distribute load evenly across the shop floor.
Same-Part
Bonus
−0.15 if last part = this part
Bonus for staying on the same part — avoids unnecessary changeover cost.
Color Bonus
−0.08 if same color
Small bonus for same-color follow-on to reduce purge probability.
ELIGIBILITY FILTERS (applied before ranking)
Compatibility matrix must show machine = 1 for this part
Effective free hours (after CO subtraction) ≥ MIN_RUN_HOURS (4h)
Runner-Lock: if inv < 2× daily, machine MUST have already run this part
Fixed-machine exclusion: non-fixed parts cannot use fixed-machine slots
Part fixed-machine: if fixed, primary candidate is always the designated machine

## Slide 14
CONSTRAINT SUMMARY & DECISION MATRIX
ID
Constraint
Type
Impact Level
Phase
C1
Min Run Hours (4h)
Hard
HIGH
Assignment
C2
Daily / Indent Thresholds
Hard
HIGH
Pre-filter
C3
OPD Ceiling (3–5 days)
Soft
MEDIUM
Assignment + Fill
C4
Terminal Inventory
Hard
CRITICAL
Pre-filter
C5
Fixed Machine (A/B Phase)
Hard
HIGH
Dedicated pass
C6
Color Purge CO (+10min)
Soft
MEDIUM
CO calculation
C7
Max Daily CO (25)
Hard
HIGH
All phases
C8
Tool Availability
Hard
HIGH
Assignment
C9
Runner Priority Lock
Hard
CRITICAL
Enforcement pass
C10
22H Utilization Target
Soft
HIGH
Enforcer + Buffer
C11
Tool-Changer Queue
Hard
MEDIUM
Post-resequence
Key Parameter
MIN_RUN_HOURS = 4
MIN_DAILY = 150 | TARGET = 5d
OPD: 3–5 days by scenario
TERMINAL_THRESHOLD dict
SAFETY_DAYS = 3 | TARGET = 5
COLOR_PURGE_HRS = 10min
MAX_DAILY_CO = 25
TOOL from sheet (1–N)
RUNNER_PRIORITY_DAYS = 2
UTIL_TARGET_PCT = 90%
MIN_CO_GAP_HRS = 20min

## Slide 15
Smart APS V11-FIXED
11 constraints. One deterministic plan. Zero idle release.
22H
Target
Utilization
11
Production
Constraints
≤25
Max Daily
Changeovers
100%
Deterministic
Output
Every constraint in the system exists to maximize parts output while respecting physical, inventory, and operational limits.
The scheduler guarantees the same plan for the same inputs — every time.
Smart APS V11-FIXED | Advanced Production Scheduling | VT Line