## Slide 1
Smart APS V11
Constraint Architecture & Logic
⏱ Time & Capacity
🔒 Fixed Machine
🧩 Compatibility
🌈 Colour Changeover
🔧 Terminal / Raw Mat.
📦 Inventory & OPD
⚡ Runner Priority
🔀 Changeover Queue
8 Constraint Domains • End-to-End Scheduling Logic

## Slide 2
Master Scheduling Flow
How all constraints chain together — top to bottom
Load Data
& Dicts
Parts, Matrix, CO
Fixed Machine
Pass
Phase A / Phase B
Scenario
Classifier
0 Critical → 3 Healthy
Priority
Scoring
Urgency·Category·Indent
Primary
Assign Pass
Tool-aware assignment
Zero-Inv
Displacement
Push aside lower-pri
Runner Priority
Enforce
< 2-day threshold
Utilisation
Enforcer
22 h target fill
Strategic
Buffer Filler
7-day ahead build
Resequence
Machine Rows
Min CO order
CO Stagger
Scheduler
Serial tool-changer queue
Stagger by
Quantity
Push/pull to create gap
Validation
Check
Min run-hrs violations
Forward Look
7-day Alert
Stock-out risk horizon
Save Machine
State
Persist last part ran
Data / Init
Decision
Output/Save
Validation
Optimisation

## Slide 3
⏱ Time & Capacity Constraint
Machine hours are the core production budget
CO
0.67h
RUN HOURS (indent-driven)
InvBuild
(OPD cap)
IDLE
→ filled
22 Hours per Machine per Day
Available Hours
Standard : 22 h / day
Extended : 23 h (Phase A fixed)
Min run block : 4 h minimum
Machines never released idle
Run-Hour Calculation
Shortfall qty = daily – inventory
Hrs needed = shortfall ÷ rate
Capped by OPD ceiling days
Extended if headroom exists
Utilisation Enforcer
Target ≥ 90 % utilisation
S0: Extend existing parts
S2: Add new compatible parts
S3/S4: Runner rerun / any-compat
Effective Run = min( Available − CO, Headroom ÷ Rate ) | Qty = Run × Rate | Util % = Used ÷ 22 × 100

## Slide 4
🚦 Skip / Scheduling Filter Constraint
Which parts enter the scheduler — and which are excluded
ALL PARTS
Has valid cycle time (rate > 0)?
SKIP ✗
Daily indent > 150 pcs?
SKIP ✗
Monthly indent hours > 4 h?
SKIP ✗
Inventory < 5-day TARGET ceiling?
SKIP ✗
Terminal constraint OK?
SKIP ✗
✓ ENTERS SCHEDULER

## Slide 5
🔒 Fixed Machine Constraint
Certain parts are locked to dedicated machines
⚠ PHASE A — Buffer Building
Trigger: ANY fixed part inventory
< SAFETY (3-day floor)
1
Pick part with LOWEST days-coverage
2
Run FULL available hours (22h / 23h extended)
3
Machine is locked — marked Phase A
4
Inventory ceiling: OPD cap applied
5
No other parts share this machine today
✅ PHASE B — OPD Steady-State
Trigger: All fixed parts have
≥ 3-day safety buffer
1
Schedule each fixed part in turn
2
Run hours = indent hours needed (min 4h)
3
OPD headroom extends production if spare
4
Remaining hours given to normal scheduler
5
Fallback: non-fixed machine if fixed full
inv < 3d × daily?
YES → Phase A
NO → Phase B

## Slide 6
🧩 Compatibility Matrix Constraint
Parts can only run on machines they are mapped to
M-01
M-02
M-03
M-04
M-05
Part-A
✓
✓
✓
Part-B
✓
✓
Part-C
✓
✓
✓
Part-D
✓
✓
Part-E
✓
✓
Part-F
✓
✓
✓
Machine Ranking Logic
Fixed machine first
if part has dedicated machine
CO penalty
base CO + colour purge hrs
Utilisation penalty
prefer less-used machines
Part-count score
machines with more parts preferred
Same-part bonus
−0.15 if same part ran last
Runner lock
if inv < 2d, only machines already running that part
Sort by cost score, then machine name (deterministic)

## Slide 7
🌈 Colour Changeover Constraint
Colour purge time is added when colour switches on a machine
BLUE
Part-A
BLUE
Part-B
PURGE
10 min
ORANGE
Part-C
PURGE
10 min
GREEN
Part-D
GREEN
Part-E
Machine timeline ▶
Last part
colour?
Same colour
as new?
Either UNKNOWN
or NEEDS_PURGE?
CO = base
+ 10 min purge
NO
NO
CO = base only
(no purge)
YES
CO = base only
(unknown skip)
YES
Changeover Time Formula
CO hrs = base_CO + purge_hrs
base_CO = machine lookup (default 40 min)
purge_hrs = 10 min if colour differs, else 0
⚠ Parts not in today's sheet are marked NEEDS_PURGE → always adds purge time regardless of colour

## Slide 8
🔧 Terminal & Raw Material Constraint
Parts blocked when required terminals have insufficient stock
Part
Selected
Does part need
a terminal?
Terminal inv
≥ threshold?
✓ OK
Schedule
No terminal needed
→ proceed
NO
⛔ BLOCKED
Not scheduled
NO
Category-Based Threshold Multiplier
Runner
Threshold = 1.0 × daily indent
Repeater
Threshold = 0.5 × daily indent
Stranger
Threshold = 0.25 × daily indent
Blocking Behaviour
Part receives 'BLOCKED — TERMINAL' reason
Listed in VT_Not_Planned with detail
Even zero-inv parts cannot override block
Shown in VT_Terminal_Status sheet
All terminals for a part must pass
Formula: threshold = TERMINAL_THRESHOLD[category] × daily_indent | If terminal_inv < threshold → BLOCKED

## Slide 9
📦 Inventory & OPD Cap Constraint
Production is bounded by safety floor and target ceiling
CRITICAL (0 days)
BELOW SAFETY (< 3 days)
BUILDING (3 – 5 days)
AT TARGET (≥ 5 days) — SKIP
↑ Current
inv
Scenario Classifier & OPD Cap
0
ALL parts critical (inv < 1 day)
OPD = 3.0 days
1
SOME parts critical
OPD = 3.0 days
2
Some parts below 3-day safety
OPD = 4.0 days
3
All parts healthy (≥ 3 days)
OPD = 5.0 days

## Slide 10
⚡ Runner Priority Constraint
Critical Runners pre-empt lower-priority parts for machine time
Unplanned
Runners
inv < 2 × daily?
(< 2-day threshold)
Free capacity
on any machine?
✓ Place directly
(free capacity)
Skip — not critical runner
NO
Find Stranger/Repeater
to yield hours
NO
Identify
victim rows
Carve/remove
hours from victim
Reclaim
hours
Place
Runner
Displacement Rules
Only Stranger / Repeater can be victims
Runners never displaced
Victim must have more days-coverage than Runner
Protects equally critical parts
Victim inv must still be ≥ SAFETY floor after carve
No stock-out created
Min 4 h must remain on victim row
Victim keeps MIN_RUN_HOURS
Least disruptive machine chosen first
Min total hours reclaimed

## Slide 11
🔀 Changeover Serial Queue Constraint
One tool-changer services all machines — COs must be sequenced
M-01
CO
M-02
WAIT
CO
M-03
CO
M-04
WAIT
CO
M-05
WAIT
CO
← Time (hours) →
Stagger Logic
Sort CO events by natural start time
Enforce 20-min min gap between COs
If gap too small → push late-start CO
If push impossible → pull early-start CO
Wait-Fill Strategy
Tool-changer arrives early → machine waits
Extended production fills the idle window
Push qty limited by OPD headroom
Extra pieces logged as stagger adjustment
Hard Limits
Max 25 COs per day total
Min 20-min gap between any two COs
Phase-A machines excluded from stagger
CO count checked before every new addition

## Slide 12
📊 Priority Scoring Constraint
Every schedulable part gets a composite score that drives sort order
URGENCY
SCORE
0.60 × gap%
+ 0.40 × velocity%
55%
+
CATEGORY
SCORE
Runner=100
Repeater=60
Stranger=20
25%
+
INDENT
SCORE
(daily ÷ max_daily)
× 100
20%
= FINAL PRIORITY SCORE
Sub-Score Formulas
Gap Score:
gap_score = (TARGET_DAYS – days_coverage) ÷ TARGET_DAYS [clamped 0→1]
Velocity:
velocity = daily_indent ÷ max(inventory, 1)
Urgency Score:
urgency = 0.60 × gap_pct + 0.40 × velocity_pct
Final Score:
final = 0.55 × urgency + 0.25 × category_score + 0.20 × indent_score
Parts sorted descending by Final Score — ties broken by part name (alphabetical) for determinism

## Slide 13
🔧 Tool Availability Constraint
Parts with multiple tools can run on parallel machines simultaneously
M-01
🔧 Tool Active
Part-XYZ running
M-02
🔧 Tool Active
Part-XYZ running
Max tools = 2
M-03
Idle / other part
M-04
Idle / other part
Part-XYZ | Tools Available: 2 → Running on M-01 & M-02 simultaneously
Part needs
more qty?
Category:
Runner/Repeater/Stranger?
Is it critical
(zero inv)?
Max
tools
No expansion needed
Stranger / Repeater → Hard cap = 1 tool
Runner (non-critical) → Cap = min(2, tools available)
Runner (critical, zero-inv) → Cap = tools available (all tools)

## Slide 14
🔄 Intra-Machine Resequencing Constraint
Parts on a machine are reordered to minimise total changeover cost
BEFORE Resequencing
Part-D
GREEN
→ CO + PURGE ⚠
Part-A
BLUE
→ CO + PURGE ⚠
Part-B
ORANGE
→ CO + PURGE ⚠
Part-C
BLUE
AFTER Resequencing
Part-D
GREEN
→ CO + PURGE ⚠
Part-C
BLUE
→ CO (base only)
Part-A
BLUE
→ CO + PURGE ⚠
Part-B
ORANGE
Resequence
min CO cost
Algorithm: seed from yesterday's last part → greedy nearest-neighbour by CO cost → stable sort tie-break on part name

## Slide 15
🔭 Forward Look & Constraint Summary
7-day horizon alert + all 8 constraint domains at a glance
22%
Day 1
18%
Day 2
14%
Day 3
9%
Day 4
5%
Day 5
2%
Day 6
0%
Day 7
⚠ BELOW SAFETY
⛔ ZERO STOCK
⏱
Time & Capacity
22h budget, 4h min run, 90% util target
🚦
Skip Filter
Rate>0, daily>150, inv<5d target, terminal OK
🔒
Fixed Machine
Phase A: full 22h build | Phase B: indent-hrs
🧩
Compatibility
Matrix-driven, ranked by cost score
🌈
Colour CO
Base CO + 10 min purge on colour switch
🔧
Terminal / RM
Category threshold: Runner 1× / Rep 0.5× / Str 0.25×
📦
Inventory & OPD
Scenario 0-3 sets OPD cap 3-5 days
⚡
Runner Priority
< 2-day inv → pre-empt with displacement
Every constraint is deterministic — same inputs always produce the same optimal plan
Machine State Persistence (Cross-Day Constraint)
Last part run on each machine is saved to machine_state.json at end of day
Next day: CO cost calculated from yesterday's last part → colour continuity enforced across days
If a saved part is no longer in today's sheet → marked NEEDS_PURGE (always adds purge time)