## Slide 1
Digital Production Planning
Moulding Section — Uno Minda Rika Pvt. Ltd.
How does the computer decide what to make, on which machine, and how much?
Prepared by: Tushar | Guided by: Mr. Amrit Lal | April 2026

## Slide 2
What Does This System Actually Do?
STEP 1
📋
Reads the Data
Checks stock in hand, monthly targets, cycle times, and machine list every morning
▶
STEP 2
🏭
Decides What to Make
Picks parts that are running low first. Runner parts ALWAYS get the first chance on machines
▶
STEP 3
⚙️
Assigns Machines
Puts each part on the best machine — one that is free and has made that part before
▶
STEP 4
📊
Writes the Plan
Gives a full day plan: which machine makes what, for how long, and expected quantity
💡 Think of it as a smart supervisor who reads all the numbers and writes the daily shift plan — automatically, every morning.

## Slide 3
What Was Happening Before vs. What Happens Now
Area | ❌ As-Is (Old Way) | ⚠️ The Gap (Problem) | ✅ To-Be (New System)
Deciding what to make | Supervisor decided based on experience or gut feeling | Some parts ran out without anyone noticing | Computer checks every part's stock and makes the list automatically
Runner parts (daily-demand parts) | Runners competed with other parts for machines | Runners sometimes missed a shift, causing stock-out | Runners ALWAYS go first — no Stranger/Repeater can take their machine
Safety stock (buffer) | No fixed rule — sometimes 1 day, sometimes 10 days stock sat idle | Either parts ran out or warehouse was overfull | 3-day safety floor + 5-day target ceiling — always in a healthy range
Terminal parts (inserts/clips) | Machine started, then worker discovered the clip was missing | Wasted moulding time, no usable parts made | System checks clip/insert stock BEFORE scheduling — zero stock = do not run
Machine time use | Machines sometimes sat idle in the middle of the shift | Lost production hours that cannot be recovered | Enforcer fills every hour of every machine — 22 hours / day target
Fixed machines | Any part could land on any machine — sometimes wrong tooling | Tool damage, quality issues, re-setup time wasted | Dedicated machines locked to their parts unless stock is full (5 days)

## Slide 4
Rule 1 — Keep the Right Amount of Stock
The Stock Meter 📊
🔴 DANGER (0 days)
Machine must run NOW. No stock left. Line will stop.
🟡 BELOW SAFETY (0–3 days)
Running low. Plan it today — do not wait.
🟢 BUILDING (3–5 days)
Healthy zone. System is slowly filling the buffer.
✅ AT TARGET (5 days)
Tank is full! Skip this part today. Don't overfill.
How the system decides how much to make today
Check today's stock for a part
▼
❓ Is stock already at 5 days?
YES →
SKIP today ✅
Stock is full
NO ▼
PLAN it today — make enough
to reach safety zone
▼
Decide how many hours to run based on how low the stock is
(Critically low = more hours | Almost at target = fewer hours)
▼
Add to today's plan ✅

## Slide 5
Rule 2 — Runner Parts ALWAYS Go First
🏃 What is a Runner?
Runner = A part that is ordered every single day. The customer cannot wait for this part. If stock runs out, the assembly line STOPS.
RANK 1
🏃
RUNNER
Daily-demand part. Line stops without it. ALWAYS planned first.
RANK 2
🔄
REPEATER
Made regularly, but not every day. Planned after all Runners.
RANK 3
👤
STRANGER
Made rarely — only when stock is very low. Gets whatever machine is left.
⚠️ The Old Problem
A Stranger part with zero stock could get a higher score than a Runner part with 1-day stock — and take the last machine slot.
The Runner then missed its shift. Next day → stock-out.

## Slide 6
Rule 2 Continued — How the System Makes Room for Runners
Runner part found with < 1 day stock
Is there a free machine?
YES → Place Runner on free machine ✅
NO → Look at all busy machines
Any machine has a Stranger or Repeater running?
Reduce that part's hours. Give freed hours to the Runner ✅
No machine can help → Log as unresolvable ❌
▼
YES →
← NO
▼
CAN displace ▲
CANNOT displace ▼
🔒 GOLDEN RULE: No Stranger or Repeater can hold machine capacity when a Runner is waiting.

## Slide 7
Rule 3 — Always Check Inserts / Clips Before Running
🔩 What is a Terminal?
Some moulded parts need a small metal clip, insert, or connector to be placed inside the mould BEFORE the plastic is injected.
This small part is called a TERMINAL.
1 terminal is used per piece produced.
❌ What Used to Happen
Machine started moulding.
⏱ After 30 minutes → Worker finds the terminal box is empty.
All pieces made = SCRAP (no insert inside).
Machine time wasted. Reset needed.
🛡️ How the System Prevents This
📋
Morning check
Before making the plan, system reads the terminal stock file
▶
🔍
Part needs terminal?
Check the mapping: does this part need a clip / insert?
▶
❌
Terminal = 0 stock
Part is BLOCKED. Not planned today. Alert raised for store team.
▶
✅
Terminal > 0 stock
Part is cleared. Added to plan. Stock reduces as pieces are made.

## Slide 8
Rule 4 — Some Machines Are Reserved for Specific Parts
🏪 Real-Life Example: Think of a reserved parking spot near the factory gate. That spot belongs to the factory ambulance. Even if the ambulance is not there right now, you cannot park your car in it — unless the ambulance is officially 'off duty'.
🔒 Machine LOCKED (stock < 5 days)
1. The dedicated part is running low (below 5 days stock)
2. This machine belongs to ONLY that part today
3. No Stranger part can use this machine — even if the machine has free hours
4. No Repeater part can use this machine
5. Only another Runner (if compatible) may use leftover hours
6. The system will show: [FIXED RESERVE] in the plan
🔓 Machine OPEN (stock ≥ 5 days)
1. The dedicated part has reached its 5-day ceiling — no need to make more today
2. Machine is free to use for other compatible parts
3. Other Runners get preference first
4. Repeaters can use it if Runners don't need it
5. Strangers may use remaining time last
6. System shows: [OPEN — 5d+ stock] in the plan

## Slide 9
Rule 5 — Use Every Minute of the Machine Wisely
🎨 Colour Changeover Penalty — 10 Minutes
If the last part was BLACK and the next part is WHITE:
→ Machine must be purged (flushed) with new material for 10 minutes
→ No good parts are made during this time
→ System adds this 10-min penalty to the changeover time
→ System prefers to run same-colour parts on the same machine to avoid purging
⏱️ 22 Hours / Day — Every Hour Counts
2 shifts × 12 hours = 24 hours
Minus 1 hour break per shift = 22 production hours
The system fills all 22 hours of every machine:
① Extend current parts first (within allowed stock limit)
② Add unplanned parts that are running low
③ Re-run Runner parts with a second tool
④ Use skipped parts as last resort
Idle machine = lost production that cannot be recovered.
🔧 Tool Changeover Queue — One at a Time
Each changeover (tool swap) needs the Tool Changer team.
Problem: Two machines cannot both need a tool change at the same time.
Solution: The system lines up all changeovers in a queue — like a token system at a government office.
Each machine waits for its turn. While waiting, the machine continues running the previous part.

## Slide 10
Master Flow — How the Plan Is Built Step by Step
📥 READ DATA
Stock, targets, machine list, terminal stock loaded
🔍 AUDIT EVERY PART
Gate 1: Missing cycle time? Gate 2: Not in matrix? Gate 3: No indent? Gate 4: Terminal zero? Gate 5: Stock already full?
🏃 SORT: RUNNERS FIRST
All parts sorted — Runners at the top, then Repeaters, then Strangers. Within each group, lowest stock goes first.
⚙️ ASSIGN MACHINES
Each part gets its best machine. Fixed machines go to their reserved parts. Same-colour preference applied.
🛡️ RUNNER SAFETY CHECK
Any Runner still not planned? System displaces Strangers/Repeaters to make room for them.
⏱️ FILL ALL 22 HOURS
Enforcer checks every machine. Any spare time → extend existing parts or add new parts.
📊 WRITE THE PLAN
Final Excel file written with per-machine plan, CO queue, stock projections, and alerts.

## Slide 11
What Comes Out — The Daily Production Plan
🏭 Machine-wise Plan
For each machine: which part, how many hours, how many pieces expected
🔧 Changeover Queue
Token system: which machine does tool change first, at what time
📦 Stock Projection
Shows stock level before and after today's production for each part
⚠️ Manual Alert List
Parts that have terminal (insert) problems — needs store team action
🏃 Runner Priority Log
Which Runners were placed by displacing other parts — full audit trail
📋 Not Planned Log
Parts that couldn't be planned today — reason listed (terminal, capacity, etc.)

## Slide 12
The 5 Golden Rules — Quick Summary
1
📊 Keep the Right Amount of Stock
3-day safety floor → 5-day target ceiling. Make more when low. Stop when full.
2
🏃 Runners Always Go First
Runner parts are sorted to the TOP of the list. No Stranger or Repeater can take their machine.
3
🔩 Check Inserts Before Starting
If any required terminal/insert has zero stock → part is BLOCKED. Machine doesn't start wasted production.
4
🔒 Respect Reserved Machines
Fixed machines belong to their parts when stock is below 5 days. Open only when stock is full.
5
⏱️ Fill Every Machine Hour
22 hours/day is the target. Spare time is filled intelligently — same colour preferred to avoid purge.

## Slide 13
Digital Production Planning
Moulding Section — Uno Minda Rika Pvt. Ltd.
Key Benefits
✅ No more stock-outs for Runner parts
✅ No wasted machine time from missing inserts/clips
✅ Fixed machines protected from wrong-part scheduling
✅ 22 hours fully utilised every day, every machine
✅ Full audit trail — every decision is recorded in the plan file
Prepared by: Tushar | Guided by: Mr. Amrit Lal | April 2026 | For internal use — Moulding Section