## Slide 1
Smart APS V6
Constraints, Solutions & Planning Logic
VT Section | Indent-Based Production Planning | Tool-Changer Scheduling
7
Hard Constraints
12
Scheduling Rules
10
Output Sheets

## Slide 2
All Constraints at a Glance
C1
Skip Rules
Parts with daily indent ≤ 150 OR full monthly indent producible in ≤ 4h are never planned
C2
Over-Production Cap
No part may accumulate more than 5 × daily_indent in stock (inventory + produced today)
C3
Tool-Changer
ONE tool changer for all 30 VT machines — no two changeovers may overlap in time
C4
Priority Order
Runner > Repeater > Stranger; within each tier, higher daily indent runs first
C5
Machine Hours
Each machine has exactly 22 available hours per shift — hard ceiling
C6
Min Run Block
No part can be assigned less than 4 continuous hours on a machine (setup minimum)
C7
Changeover State
First run = clean slate (no CO charged). From day 2, CO charged only when last part differs

## Slide 3
C1 — Skip Rules
Parts that are never planned regardless of inventory
Part enters check
daily_indent ≤ 150?
SKIP
(Too Small)
YES
NO
monthly_indent / rate ≤ 4h?
SKIP
(Trivial Run)
YES
NO
Enters Scheduler
⚠ ABSOLUTE RULES
• Zero inventory is NO exception • Both conditions are independent • Either one triggers a skip • Checked before anything else
Skip rules are hardcoded in Section 2: MIN_DAILY_INDENT = 150 | MIN_INDENT_HOURS = 4.0

## Slide 4
C2 — Over-Production Cap
Prevent a single part from consuming machine time far beyond its need
today_target = max(0, daily_indent − inventory) headroom = max(0, 5 × daily_indent − inventory) capped_target = min(today_target, headroom)
Compute
today_target
Compute
5-day headroom
capped_target =
min(target, headroom)
Assign
hours
Worked Example
Part X: daily_indent = 321 | inventory = 0 | rate = 400 pcs/hr today_target = max(0, 321 − 0) = 321 units → 0.80 hours headroom = max(0, 5×321 − 0) = 1605 units → 4.01 hours capped_target = min(321, 1605) = 321 → machine runs 0.80h ✓ (NOT 21h)

## Slide 5
C3 — Single Tool-Changer Constraint
ONE tool changer serves ALL 30 VT machines — no two changeovers may overlap
The Problem
M1
CO
M2
CO
M3
CO
Conflict!
All 3 COs
overlap
The Solution (CSP)
M1
CO
M2
+run
CO
M3
+run
CO
CSP Algorithm — 3 Steps
Step 1 — COLLECT
Extract all CO events from plan across all 30 machines with natural start times
Step 2 — CSP SOLVE
python-constraint finds optimal queue order: no two CO intervals [start, start+dur] overlap
Step 3 — ASSIGN
Walk queue in order. If machine must wait → extend run before CO to fill idle time (never waste)

## Slide 6
C3 — Tool-Changer CSP Flowchart
All CO events collected
(across 30 machines)
Sort by natural start time
CSP: assign start slots
(no-overlap constraint)
actual_start > natural_start?
YES
(wait)
Extend run before CO
by wait duration
Extra pieces gained
(no idle time ✓)
NO
(on time)
CO starts immediately
No adjustment needed
Advance TC free_at
+= CO duration
Next CO event
Loop until all CO events processed

## Slide 7
C4 — Priority Order: Runner > Repeater > Stranger
Within each tier, higher daily_indent runs first — biggest need gets machine time first
RUNNER
Tier 0
Dedicated machine. Cap = today_target + 1-day buffer.
Runner machines excluded from Repeaters/Strangers.
REPEATER
Tier 1
Runs on any non-Runner machine.
Sorted by daily_indent desc within this tier.
STRANGER
Tier 2
Lowest priority. Only gets machine time after all
Runners and Repeaters have been allocated.
Sort Key:
sort_values( [Tier ASC, Daily_Indent DESC] ) → Runner with indent=500 ranks #1. Stranger with indent=600 still ranks after ALL Runners.

## Slide 8
C5 & C6 — Machine Hours Cap + Minimum Run Block
C5 — 22-Hour Machine Ceiling
Available hours per shift: 22h machine_hours[m] ≤ 22h at all times Enforced in: • Primary assignment (run_h capped) • Filler extension (spare calc) • CSP stagger (extend only if spare exists) Utilisation Status: FULL ≥ 21.5h | GOOD ≥ 18.7h
PARTIAL ≥ 11h | UNDERUSED < 11h
C6 — Minimum 4-Hour Run Block
MIN_RUN_HOURS = 4h No part assigned less than 4h on a machine — not enough to justify setup. Enforced in: • rank_machines: effective_free < 4h → machine skipped • run_assignment: run_h = max(run_h, MIN_RUN_HOURS) • filler Option B: eff_run < 4h → candidate skipped After changeover: effective_free = machine_free − CO_hrs
if effective_free < 4h → machine not eligible

## Slide 9
C7 — Changeover State & Clean Slate Logic
machine_state.json saves last-run part per machine — drives CO decisions from day 2
machine_state.json
exists?
YES
Load last-run
part per machine
NO
FIRST RUN
Clean Slate
last[m] = None
→ CO = 0h all
machines
last[m] == today's
planned part?
YES
CO = 0h
(same mould loaded)
NO
CO = changeover
dict[m]
None
(1st run)
CO = 0h
(unknown = clean)
Assign part to machine
Update last[m] = part
Save machine_state.json
(used tomorrow)

## Slide 10
End-to-End Planning Flow
1. Load VT Sheet
Part, Indent, Cycle time,
Cavity, Inventory, Category
2. Compute Rate
Rate = 3600 / cycle_time
(cavities cancel out)
3. Apply Skip Rules
daily≤150 OR monthly/rate≤4h
→ SKIP (absolute)
4. Check Inventory
inv ≥ daily_indent
→ Not Required Today
5. Priority Sort
Runner > Repeater > Stranger
then daily_indent DESC
6. Assign Machines
Rank by CO cost, capacity.
Cap = 5× daily_indent
7. 22-hr Filler
Fill spare time. No blocking.
Cap at 5-day overproduction
8. CSP Tool-Changer
Serialize all COs. Extend runs
to fill waits. No overlap.
9. Save & Export
10 Excel sheets. machine_state
saved for tomorrow.

## Slide 11
Output Sheets — What Each Sheet Tells You
VT_Plan_By_Machine
Machine-wise schedule: sequence, start/end times, CO, run hours, rate, qty
VT_Plan
Flat plan: all planned parts with full detail including rate, indent, target
VT_Daily_Indent_Status
Which parts MEET / MISS daily indent — production alone vs with inventory
VT_Machine_Util
Utilisation per machine: used/unused hours, changeovers, part rates
VT_Not_Planned
Parts needed but not planned — with exact reason (capacity / matrix / etc)
VT_Not_Required_Today
Parts where inventory already covers daily indent — deferred to tomorrow
VT_Skipped_Parts
Parts excluded by skip rules — daily≤150 or monthly/rate≤4h
VT_Inventory_Health
After-today inventory = inv + produced. Days of coverage per part
VT_Indent_Horizon
Full indent breakdown: monthly, daily, target, rate, status per part
VT_Part_Audit
Gate-by-gate trace of ALL 142 VT parts — why each is planned or excluded

## Slide 12
Key Design Decisions & Rationale
Why daily_indent ≤ 150 skip?
Parts with < 150 daily need take machine time away from critical parts — not worth a setup
Why ≤ 4h monthly skip?
The entire month's need can be produced in one short burst — plan it on demand, not daily
Why 5× daily cap?
Allows reasonable buffer without blocking other parts. 28× was causing starvation
Why CSP for tool-changer?
Greedy sort can't guarantee global no-overlap. CSP finds provably valid ordering every time
Why extend runs instead of reduce?
Extending fills idle machine time and produces more. Reducing loses production permanently
Why clean slate on day 1?
No historical data = no basis to charge CO. Penalising unknown history is unfair to all parts
Why Runner > Repeater > Stranger?
Runners are critical, high-frequency parts. They must never be starved of machine time